## Slide 1: PCB Order Specification
PCB name: 901_10089 V3
Number of PCBs: 50-pcs
Number of Layers: single layer double surfaces
Finished Overall Thickness: 0.238mm (0.017 top Cu + 0.203 RO4003C +0.017 bottom Cu)
Material Type(s): Rogers RO4003C with 1/2oz Cu clads
Exterior Board Dimensions: 28 x 25 mm
a: Manufacturing Rails for Assembly No
Smallest Finished Hole Size: 0.3mm
Pad Size Used for the Smallest Finished Hole Size:
Surface Finish(s): 30um-in minimum, Soft-gold plating
Solder mask Color: Green
Electrolytic Gold Edge Connectors (aka fingers): No
Edge Mill, Back-Drill, Countersinks or Counterbores: no
Through Hole Via Fill Required: Solid Copper filled for center portion (shown in next page). Cu-paste is not acceptable.
Other holes are normal plated through holes.
Impedance Controlled and Tolerance: no
Board Rotation on Manufacturing Processing Panel: no
ITAR yes or No: No

## Slide 2: PCB Order Specification
This portion requires Cu filled Vias

## Slide 3: PCB Order Specification
Top side
Bottom side